## Slide 1: IPv6 Intro Part 2: Address Types and Application
Notes: SCRIPT:
Welcome, this is the second of 2 lessons that introduce Internet Protocol, version 6 or IPv6. These two lessons combined provide information on the purpose and benefits of IPv6 as well as an explanation of the addressing structure.

## Slide 2: Objectives
Describe IPv6 address types and special addresses.
Describe IPv6 Unicast addresses and assignment methods.
Explain the stateless autoconfiguration process.
Describe IPv6 Multicast addresses and their use.
Describe IPv6 subnetting and aggregation
Configure and verify IPv6 addressing on networking devices.
Notes: SCRIPT:
This objectives of this lesson, IPv6 Intro Part 2, are to provide additional details on IPv6 address types with a focus on unicast and multicast addresses. This lesson describes methods of address assignment including stateless autoconfiguration. IPv6 subnetting and address aggregation are also discussed. The final section provides information on configuration and verification of IPv6 on networking devices.

## Slide 3
IPv6 Address Types
Notes: SCRIPT:
This section provides additional details on IPv6 address types with a focus on unicast and multicast addresses.

## Slide 4: IPv6 Addressing Space Overview
Prefix Hex Value | Use
0000 to 00FF | Unspecified Loopback IPv4-compatible
0100 to 01FF | Unassigned (0.38 % of IPv6 space)
0200 to 03FF | NSAP Network Service AP)
0400 to 1FFF | Unassigned (~11% of IPv6 space)
2000 to 3FFF | Aggregatable global unicast (12.5%)
4000 to FE7F (Huge) | Unassigned (~75% of IPv6 space)
FE80 to FEBF | Link-local
FC00 to FCFF | Unique-local
FF00 to FFFF | Multicast
Note: IPv6 Internet uses 2001::/3 which is < 2% of IPv6 address space
Notes: SCRIPT:
As we have seen in Lesson 1, the IPv6 address space is very large.
The first four Hexadecimal digits or prefix help to classify the various blocks of IPv6 addresses. The ability to identify an address type by its prefix is essential to gaining an understanding of IPv6.
In the table, the prefixes highlighted in red are important ones to remember.
The largest block of assignable addresses, from Hex 2000 to Hex 3FFF, is known as the aggregatable global unicast range which represents approximately 12.5% of the total IPv6 address space. From this range, only addresses from 2001::/3 are currently being assigned by IANA for public use on the IPv6 Internet. This is less than 2% of the total IPv6 address space.

## Slide 5: Special IPv6 Addresses
IPv6 Address | Description
::/0 | All networks and used when specifying a default static route. It is equivalent to the IPv4 quad-zero (0.0.0.0)
::/128 | Unspecified address and is initially assigned to a host when it first resolves its local link address
::1/128 | Loopback address of local host Equivalent to 127.0.0.1 in IPv4
FE80::/10 | Link-local unicast address Similar to the Windows autoconfiguration IP address of 169.254.x.x
FF00::/8 | Multicast addresses
All other addresses | Global unicast address
Notes: SCRIPT:
A closer look at some of the special IPv6 addresses and prefixes reveals similarities to IPv4.
The ones shown here are particularly helpful to remember.
For example, IPv6 address ::/0 is analogous to IPv4 quad zero address 0.0.0.0 for use in defining static default routes.
IPv6 ::1/128 is analogous to IPv4 local host loopback address 127.0.0.1.

## Slide 6: IPv6 Unicast Addresses
Link-local (FE80::/10)
Address Assignment
Global Routable
Address Assignment
Static
IPv6 Address
IPv6 Unnumbered
Dynamic
Stateless Autoconfiguration
DHCPv6
Static
IPv6 Address
IPv6 Unicast
Address Assignment
Automatically created (EUI-64 format) if a global unicast IPv6 address is configured
Dynamic
Notes: SCRIPT:
As with IPv4, Unicast is the largest and most important category of IPv6 addresses.
The two most important address types in this category are Link-local and Global Routable addresses.
Link-local addresses are used for communication between devices on a particular link.
Global routable addresses are assigned to end devices for communication over the Internet.
Each of these can be created either statically or dynamically as we will see later in this lesson.

## Slide 7: IPv6 Link-Local Unicast Address
Link-local addresses play a crucial role in the operation of IPv6.
They are dynamically created using a link-local prefix of FE80::/10 and a 64-bit interface identifier.
128 bits
FE80 1111 1110 1000 0000 0000 0000 ... 0000 0000 0000 | Interface ID
/10
FE80::/10
/64
Notes: SCRIPT:
Link-local addresses play an important role in the operation of IPv6.
They are used for automatic address configuration, neighbor discovery, router discovery, and by many routing protocols.
Packets with a link-local destination must stay on the link where they have been generated.
Routers that could forward them to other links are not allowed to do so because there has been no verification of uniqueness outside the context of the origin link.
Although link-local addresses are not routable they are often used by routing protocols for neighbor communication and updates.

## Slide 8: IPv6 Link-Local Unicast Address
R2# ping FE80::202:16FF:FEEB:3D01
Output Interface: serial0/0/0
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to FE80::202:16FF:FEEB:3D01, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 31/34/47 ms
When pinging another device using a link-local address, the outgoing interface must be specified.
Notes: SCRIPT:
  When communicating using a link-local address, the outgoing interface must be specified because every IPv6 interface is connected to FE80::/10.
  For example, if you ping the neighbor’s link-local address, you will be asked to input the interface from which you wish to ping.
  Abbreviations such as S0/0/0 are not accepted, you must enter the full name of the interface (serial0/0/0).
  Note that just enabling IPv6 on a router interface (Ethernet or Serial) and/or assigning the interface an IPv6 routable unicast address automatically creates a link-local address.

## Slide 9: IPv6 Link-Local Unicast Address Example
R1# show ipv6 interface loopback 100
Loopback100 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::222:55FF:FE18:7DE8
No Virtual link-local address(es):
Global unicast address(es):
2001:8:85A3:4290:222:55FF:FE18:7DE8, subnet is 2001:8:85A3:4290::/64 [EUI]
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF18:7DE8
MTU is 1514 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ICMP unreachables are sent
ND DAD is not supported
ND reachable time is 30000 milliseconds (using 31238)
Hosts use stateless autoconfig for addresses.
R1#
Notes: SCRIPT:
  The output from the show ipv6 interface command displays the Link-local address, which begins with FE80.
  The global unicast address, which begins with 2001, is also displayed. Global unicast addresses will be covered next.

## Slide 10: IPv6 Global Unicast Address
A global unicast address is an IPv6 address from the global public unicast prefix (2001::/16).
These addresses are routable on the global IPv6 Internet.
Global unicast addresses are aggregated upward through organizations and eventually to the ISPs.
Notes: SCRIPT:
A global unicast address is an IPv6 address from the global public unicast prefix (2001::/16).
These addresses are routable on the global IPv6 Internet.
The structure enables aggregation of routing prefixes to reduce the number of routing table entries in the global routing table.
Global unicast addresses are aggregated upward through organizations and eventually to the ISPs.
Additional information on IPv6 address aggregation is provided later in this lesson.

## Slide 11: IPv6 Global Unicast Address
The global unicast address consists of:
  A 48-bit global routing prefix
  A 16-bit subnet ID
  A 64-bit interface ID
Global Routing Prefix
Subnet
ID
Interface ID
2001 0010 | 0008 |  |  | 21B:D5FF:FE5B:A408
/23
Registry
/32
ISP Prefix
/48
Site Prefix
/64
Subnet Prefix
Notes: SCRIPT:
1. The routable global unicast address typically consists of three parts:
  The first 48 bits of the address is the global routing prefix, which is assigned by an ISP and is derived from a /32 ISP prefix.
  The next 16 bits is the subnet ID (/49 thru /64), which may be use internally by an organization to subdivide its networks.
  The remaining 64 bits of the address is the device interface ID, typically in EUI-64 bit format, which will be discussed later.

## Slide 12: IPv6 Global Unicast Address
The current IANA global routing prefix uses the range that starts with binary 0010 (2000::/3).
Global Routing Prefix
Subnet
ID
Interface ID
2001 0010 | 0008 |  |  | 21B:D5FF:FE5B:A408
/23
Registry
/32
ISP Prefix
/48
Site Prefix
/64
Subnet Prefix
Notes: SCRIPT:
  The current IANA global routing prefix uses the range that starts with binary 0010 (2000::/3).
  Addresses with a prefix of 2000::/3 (0010) to E000::/3 (1110) are required to have 64-bit interface IDs in the extended universal identifier (EUI)-64 format.
  IPv6 prefix allocation is defined by policies at IANA and the regional registries.

## Slide 13: IPv6 Global Unicast Address
The subnet ID can be used by an organization to create their own local addressing hierarchy.
Global Routing Prefix
Subnet
ID
Interface ID
2001 0010 | 0008 |  |  | 21B:D5FF:FE5B:A408
/23
Registry
/32
ISP Prefix
/48
Site Prefix
/64
Subnet Prefix
Notes: SCRIPT:
The subnet ID can be used by an organization to create their own local addressing hierarchy.
This 16-bit field allows up to 65,536 individual subnets.
This is comparable to an IPv4 Class A address such as 10.0.0.0/8 with 16 bits of subnetting using a /24 mask, however the IPv4 network/subnet combination will allow on 256 hosts per subnet and the IPv6 combination allows a huge number of hosts per subnet (2 to the 64th power).

## Slide 14: IPv6 Global Unicast Address Example
R1# show ipv6 interface loopback 100
Loopback100 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::222:55FF:FE18:7DE8
No Virtual link-local address(es):
Global unicast address(es):
2001:8:85A3:4290:222:55FF:FE18:7DE8, subnet is 2001:8:85A3:4290::/64 [EUI]
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF18:7DE8
MTU is 1514 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ICMP unreachables are sent
ND DAD is not supported
ND reachable time is 30000 milliseconds (using 31238)
Hosts use stateless autoconfig for addresses.
R1#
Notes: SCRIPT:
In the sample output from the show ipv6 interface command, the /48 address assigned by the ISP is 2001:8:85A3, represented by three 16-bit fields. Note that the second 16-bit field (with a value of Hex 0008) has the three leading zeros suppressed.
The subnet number is Hex 4290 (which translates to the 17,040th subnet decimal)
The interface address is 222:55FF:FE18:7DE, which is the EUI-64 host portion of the address.
Also note that the /64 subnet is also clearly identified as highlighted in the output in green.

## Slide 15: IPv6 Multicast Addresses
Multicasting is at the core of many IPv6 functions and is a replacement for the broadcast address.
They are defined by the prefix FF00::/8.
/16
/8
FF00::/8
128 bits
F F 1111 1111 | 0 0 00xx xxxx | Group ID
Notes: SCRIPT:
Multicasting is key to many IPv6 functions and it serves a similar function as with IPv4.
With IPv6 it is also a replacement for the broadcast address.
IPv6 multicast addresses are defined by the prefix FF00::/8.
An interface may belong to any number of multicast groups.

## Slide 16: IPv6 Multicast Address
F F 1111 1111 | 0 0 00xx xxxx | Group ID
The second octet of the address contains the prefix and transient (lifetime) flags, and the scope of the multicast address.
Flags |  |  |  | Scope
0 | 0 | P | T | xxxx
8 bits
Flags:
P = Prefix for unicast-based assignments
T = 0 if permanent, 1 if temporary
Scope:
1 (0001) = Node
2 (0010) = Link
5 (0101) = Site
8 (1000) = Organization
E (1110) = Global
/16
/8
128 bits
Notes: SCRIPT:
The first octet of a multicast address is always Hex FF or decimal 255 (or eight binary ones).
The second octet of the address contains the prefix and transient (lifetime) flags, and the scope of the multicast address.

## Slide 17: IPv6 Multicast Address
The multicast addresses FF00:: to FF0F:: are permanent and reserved.
Flags |  |  |  | Scope
0 | 0 | P | T | xxxx
8 bits
Flags:
P = Prefix for unicast-based assignments
T = 0 if permanent, 1 if temporary
Scope:
1 (0001) = Node
2 (0010) = Link
5 (0101) = Site
8 (1000) = Organization
E (1110) = Global
/16
/8
128 bits
F F 1111 1111 | 0 0 00xx xxxx | Group ID
Notes: SCRIPT:
The multicast addresses FF00:: to FF0F:: have the T flag set to 0 and are therefore permanent and reserved.
For example, a multicast address starting with FF02::/16 is a permanent address.
The last 4 bits of the /16 prefix represent the scope. For example, the scope of FF05 is site specific (Decimal 5 is binary 0101) and is used by Network Time Protocol (NTP) with IPv6.

## Slide 18: Reserved IPv6 Multicast Addresses
Reserved Multicast Address | Description
FF02::1 | All nodes on a link (link-local scope).
FF02::2 | All routers on a link.
FF02::9 | All routing information protocol (RIP) routers on a link.
FF02::1:FFxx:xxxx | All solicited-node multicast addresses used for host autoconfiguration and neighbor discovery (similar to ARP in IPv4). The xx:xxxx is the far right 24 bits of the corresponding unicast or anycast address of the node.
FF05::101 | All Network Time Protocol (NTP) servers.
Notes: SCRIPT:
Some examples of reserved IPv6 multicast address are listed here.
IPv6 multicast address FF02::9 represent all RIP routers on a link.
This is analogous to multicast address 224.0.0.9 for RIPv2 routers used with IPv4.
Address FF02::1:FFxx:xxxx is a solicited-node multicast addresses and is used for host autoconfiguration and neighbor discovery.
It serves a function similar to ARP in IPv4.

## Slide 19: IPv6 Multicast Address Example
R1# show ipv6 interface loopback 100
Loopback100 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::222:55FF:FE18:7DE8
No Virtual link-local address(es):
Global unicast address(es):
2001:8:85A3:4290:222:55FF:FE18:7DE8, subnet is 2001:8:85A3:4290::/64 [EUI]
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF18:7DE8
MTU is 1514 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ICMP unreachables are sent
ND DAD is not supported
ND reachable time is 30000 milliseconds (using 31238)
Hosts use stateless autoconfig for addresses.
R1#
Notes: SCRIPT:
With the solicited-node multicast addresses FF02::1:FFxx:xxxx, xx:xxxx is the far right 24 bits of the corresponding unicast or anycast address of the node.

## Slide 20: Solicited-Node Multicast Addresses
The solicited-node multicast address (FF02::1:FF) is used for:
  Neighbor discovery (ND) process
  Stateless address autoconfiguration
The Neighbor discovery (ND) process is used to:
  Determine the local-link address of the neighbor
  Determine the routers on the link and default route
  Keep track of neighbor reachability
  Send network information from routers to hosts
Notes: SCRIPT:
The solicited-node multicast address (FF02::1:FF) is used for the neighbor discovery (ND) process and stateless address autoconfiguration.
The Neighbor discovery (ND) process is very important function in IPv6.
It is used to determine the local-link address of a neighbor, the routers on the link and default route.
It actively keeps track of neighbor reachability and sends network information from routers to hosts.

## Slide 21: Neighbor Discovery ICMPv6 Packet Types
Neighbor Discovery uses four ICMPv6 packet types
ICMPv6 Message | Type | Description
Neighbor Solicitation (NS) | 135 | Sent by a host to determine the link-layer address of a neighbor. Used to verify that a neighbor is still reachable. An NS is also used for Duplicate Address Detection (DAD).
Neighbor Advertisement (NA) | 136 | A response to a NS message. A node may also send unsolicited NA to announce a link-layer address change.
Router Advertisement (RA) | 134 | RAs contain prefixes that are used for on-link determination or address configuration, a suggested hop limit value and MTU value. RAs are sent either periodically, or in response to a RS message.
Router Solicitation (RS) | 133 | When a host is booting it sends out an RS requesting routers to immediately generate an RA rather than wait for their next scheduled time.
Notes: SCRIPT:
Neighbor Discovery uses four ICMPv6 packet types as described in the table:
Neighbor Solicitation and Neighbor Advertisement ICMPv6 messages are used to determine link-layer addresses, neighbor reachability and for duplicate address detection (DAD).
Router Solicitation and Router Advertisement ICMPv6 messages are used between hosts and routers to communicate prefixes and facilitate on-link determination or address configuration.

## Slide 22: Neighbor Solicitation Example
ICMPv6 Neighbor Solicitation (NS) is similar to IPv4 ARP.
For Host A to send a packet to Host B it needs the MAC address of Host B.
A
B
ICMP type: 135 (NS)
Source: A
Destination: Solicited-node multicast of B (FF02::1:FFxx.xxxx)
Data: Link-layer address of A
Query: What is your link-layer address?
Notes: SCRIPT:
ICMPv6 Neighbor Solicitation (NS) is similar to IPv4 ARP in that it is used when resolving an IPv6 address to a MAC address.
In the example, Host A needs to send a packet to Host B but needs the MAC address of host B.
Host A sends a Neighbor Solicitation (ICMPv6 message type 135) on the link.
The source address is the IPv6 unicast address of the source node, Host A.

## Slide 23: Neighbor Advertisement Example
Each destination node that receives the NS responds with an ICMPv6 message type 136, NA, including Host B.
A
B
ICMP type: 136 (NA)
Source: B
Destination: A
Data: Link-layer address of B
A
B
A and B can now exchange packets on this link.
Notes: SCRIPT:
Each destination node that receives the NS responds with an ICMPv6 NA message type 136.
The source address of this message is the IPv6 address of the responding node, and the destination address is the IPv6 address of the original source node (which sent the NS).
The data portion includes the link-layer address of the destination node (Host B).
The two devices can now communicate on the link because they know each other’s link-layer addresses.

## Slide 24: Stateless Address Autoconfiguration (SLAAC)
Every IPv6 system (other than routers) is able to build its own unicast global address.
    Enables new devices to easily connect to the Internet.
    No configuration or DHCP servers is required.
IPv6 Router - sends network-type info on local link.
    IPv6 prefix
    Default IPv6 route
IPv6 Hosts - listen on local link and configure themselves.
      IP Address (EUI-64)
      Default route
Notes: SCRIPT:
Stateless address autoconfiguration offers new functionality in IPv6.
Every IPv6 system (other than routers) is able to build its own unicast global address.
  This enables new devices such as cellular phones, wireless devices, home appliances, and home networks, to easily connect to the Internet.
  No configuration or DHCP servers are required.
An IPv6 router periodically sends network-type information on the local link using a Router Advertisement (RA).
This includes the IPv6 prefix and default IPv6 route for use by hosts.
IPv6 workstations and servers listen on the local link and configure themselves with an IPv6 Address and a default route.
The IPv6 address is created by appending the host link-layer (MAC Address) in EUI-64 (Extended Unique Identifier) format to the /64 prefix sent by the router.

## Slide 25: Stateless Address Autoconfiguration
IPV6 Host
IPV6 Router
Router sends network info
(IPV6 Prefix and Default IPv6 Route)
Local Link
MAC Address
00:14:BF:7A:3C:E5
Autoconfiguration Address
(IPv6 Prefix + Link-Layer EUI Address)
RA
Notes: SCRIPT:
Shown here is a basic illustration how Autoconfiguration enables a host to configure its own IPv6 address (and default gateway) using a Router Advertisement (RA).
When a host is booting it sends out a Router Solicitation (RS) requesting routers to immediately generate an RA rather than wait for their next scheduled RA.

## Slide 26: Ethernet EUI-64 IPv6 Addresses
The first 64 bits are the network portion of the address and are specified or learned via SLAAC.
The interface ID (second 64-bits) is the host portion of the address and is automatically generated by the router or host device.
The interface ID on an Ethernet link is based on the 48-bit MAC address of the interface with an additional 16-bit 0xFFFE inserted in the middle of the MAC address.
Notes: SCRIPT:
EUI-64 IPv6 addresses are addresses where the first 64 bits are the network portion of the address and are either specified or learned via stateless autoconfiguration.
The interface ID (second 64-bits) is the host portion of the address and is automatically generated by the router or host device.
The interface ID on an Ethernet link is based on the 48-bit MAC address of the interface with an additional 16-bit 0xFFFE inserted in the middle of the MAC address.
This creates an extended unique identifier referred to as the EUI-64 format.
EUI-64 addresses can be generated on IPv6 router interfaces and on IPv6 hosts.

## Slide 27: EUI-64 IPv6 Interface Identifier
48-bit MAC Address
64-bit IPv6 EUI-64 Interface ID
Notes: SCRIPT:
The EUI-64 standard inserts a 16-bit 0xFFFE in the middle at the 24th bit of the MAC address to create a unique 64-bit interface identifier.
The seventh bit in the high-order byte is set to 1 to indicate the uniqueness of the interface ID.

## Slide 28: Stateless Autoconfiguration Process
A
ICMP type: 133 (RS)
Source: ::
Destination: All routers multicast address (FF02::2)
Query: Please send RA
R1
A
R1
ICMP type: 134 (RA)
Source: R1 link-local address
Destination: All nodes multicast address (FF02::1)
Data: Options, prefixes, lifetime, …
Notes: SCRIPT:
This graphic provides some additional details on how the Host/Router autoconfiguration process works.
When it boots up, Host A sends a router solicitation (RS) message to the “All Routers” multicast address (FF02::2) requesting a router advertisement (RA).
Router R1 on the link responds with an RA to the “All Nodes” multicast address (FF02::1) so that Host A has the information it needs to autoconfigure its IPv6 address.
  The prefix included in the RA is used as the /64 prefix for the host address.
  The interface ID used is the EUI-64 format interface ID for the host.

## Slide 29: Stateless Autoconfiguration Process
Host A creates a link-local address and solicited-node address using the RA supplied by the router.
Host A verifies that it’s new IPv6 address is unique using DAD process.
ICMP type: 135 (NS)
Source: ::
Destination: Solicited-node address of A
Data: Link-layer address of A
Query: What is your link-layer address?
A
B
Notes: SCRIPT:
The host now creates a link-local address and solicited-node address using the RA supplied by the router.
Next it needs to verify that it’s new IPv6 address is unique on the link using the Duplicate Address Detection (DAD) process.
  DAD is used during the autoconfiguration process to ensure that no other device is using the autoconfiguration address.
  During the DAD phase, Host A sends an NS to query if another node on the link has the same IPv6 address.
  If a node responds to the request, it means that the IPv6 address is already in use, and Host A needs to be manually configured.

## Slide 30: IPv6 Subnetting and Aggregation
Notes: SCRIPT:
This section provides basic information on IPv6 subnetting and address aggregation.

## Slide 31: IPv6 Subnetting Overview
Not the same as IPv4
IPv6 does NOT use subnet masks
CIDR notation is used
  IPv6 address is in Hex
  Network mask in decimal
Number of subnet bits set to 1 define network prefix
All other bits are for nodes
There are no reserved addresses (network or broadcast)
2001:25:12:ab12:3456:dfb5:712:45FF/64
Notes: SCRIPT:
IPv6 subnetting is based on the network address assigned by the ISP and the needs of the organization to subdivide that space.
In this example, The network address assigned to the organization is 2001:25:12 (the first 48 bits).
The site prefix is /48 decimal and the site prefix plus subnets (ab12) is /64.
IPv6 uses the same notation as CIDR in IPv4, there are no subnet masks, only a slash and a decimal number representing the number of bits in the network/subnet.
In addition, there are no reserved subnet addresses (network or broadcast) with IPv6 so it is not necessary to account for the first and last address on a subnet when determining the number of valid host addresses (no more n^2 – 2).

## Slide 32: Prefix Length, Allocation of Bits
Example: 2001:DB8:0:2F00:2AA:FF:FE28:9C5A/64
Prefix length (total number of network bits) is 64
16 subnet bits allow 65,535 LANs
Usually 64 bits are used for hosts in IPv6
Notes: SCRIPT:
IPv6 uses CIDR notation, as does IPv4, to identify the prefix length.
The normal prefix length (total number of network bits) for an IPv6 address is 64.
The rightmost 16 bits (/49 to /64) allow for 65,535 LANs.
IPv6 does NOT use subnet masks.

## Slide 33: IPv6 Subnetting with Global Unicast Addresses
The global routing prefix is assigned to a service provider by IANA (/32).
The site level aggregator (SLA) is assigned by the ISP (/48).
The LAN ID represents individual subnets within the customer site and is administered by the customer (/64).
Notes: SCRIPT:
The global routing prefix (/32) is assigned to a service provider by the Internet Assigned Numbers Authority (IANA).
The next 16 bits is the SLA or site level aggregator and is a /48 network address assigned to a customer by their service provider. The SLA can be viewed as a subnet ID from the ISPs perspective.
The 16-bit LAN ID represents individual networks within the customer site and is administered by the customer.
The total network ID is comprised of the Global prefix (32 bits), The SLA (16 bits) and the LAN subnet ID (16 bits) resulting in a prefix length of /64.
The remaining 64 bits are the Interface ID and represent an individual host on a subnet or LAN.

## Slide 34: IPv6 Subnetting with Global Unicast Addresses
Default Subnets
  /23 Registry
  /32 ISP Prefix
  /48 Site Prefix
    Bits 49 to 64 are for subnets
    2^16 = 65,535 subnets available
  /64 Default Subnet prefix
    Bits 65 to 128 for Hosts
    Host bits are either, EUI-64, DHCP, Random number generated
2001
0DB8
0001
0001
Interface ID
/23
Registry
/32
ISP
/48
Site
/64
Subnet
64 bits
Notes: SCRIPT:
This summarizes the prefix lengths and subnet/host structure of a standard IPv6 global unicast address.

## Slide 35: IPv6 Subnetting with Global Unicast Addresses
IPv6 prefix | # of Subnets | # of Hosts
2001:520:1:1::3FFF /128 | 1 | 1
2001:520:0:1:: /64 (default prefix for subnet) | 1 | 2^64
2001:520:0:: /48 (default Site prefix) | 2^16 | 2^64 per subnet
61 Global Network bits and 64 Host bits
No more “bit borrowing” as with IPv4
2^64 hosts possible in a single broadcast domain
Autoconfiguration will take care of most of them
VLANs become the method of isolation
Notes: SCRIPT:
The first three bits are fixed (001) which results in 61 Global Network bits and 64 Host bits.
You do NOT get to “borrow” host bits any more (nor is it necessary, as it was with IPv4, due to the huge IPv6 address space)
2^64 hosts are theoretically possible in a single broadcast domain
With autoconfiguration it is not necessary to configure them.
Host devices can be moved around and they’ll automatically generate their EUI-64 addresses.
VLANs become the method of isolation.

## Slide 36: IPv6 Address Hierarchy
Internet Registries
Tier-1 Provider
Tier-2 Provider
Tier-n Provider
Organizations
Sites
Hosts
Large address space
Allows for multiple levels
Notes: SCRIPT:
The large IPv6 address space is hierarchical by design which allows for multiple levels, greatly facilitating address assignment and aggregation.

## Slide 37: IPv6 Address Aggregation
Large prefix for an organization
  Can handle entire network
ISPs summarize routes
  All customer prefixes into one prefix
  Make it available to the Internet
Aggregation provides:
  Efficient routing
  Scalable routing
  Fewer routes in global IPV6 routing table
Notes: SCRIPT:
The IPV6 address space is huge and hierarchical.
A prefix can be assigned to an organization that can handle the entire network, even for very large organizations, and still have plenty of room for future growth.
ISPs summarize routes so that all customer prefixes can be aggregated into one prefix and made available to the Internet.
Aggregation provides efficient and scalable routing and fewer routes in the global IPV6 routing table with an enforced hierarchical VLSM model.

## Slide 38
Customer A1
Customer A2
ISP A
AS 60000
2001:051A::/35
2001:051A:A1::/48
2001:051A:A2::/48
Routing Table
2001:051A:A1::/48 AS 60000
2001:051A:A2::/48 AS 60000
Global Routing Table
2001:051A::/35
Aggregation Example
Notes: SCRIPT:
In this example, all subnets of the /48 networks assigned to Customers A1 and A2 can be summarized by ISP A to a single /35 network address to be advertised to the Internet.
Note that if the customer changes their provider, they must change the IPv6 Prefix.

## Slide 39: Subnetting Global Addresses
2001:05a8::0/32
Subnets the ISP can create:
  2^16 = 65,536
  2001:05a8:0001::0 – 2001:05a8:ffff::0/48
Notes: SCRIPT:
In this example, an ISP has been assigned a /32 address by the regional registry. This leaves 16 SLA bits which yields 65,535 /48 networks that can be assigned to various customer sites.

## Slide 40: Subnetting Global Addresses
Customer now has 16 network bits with which to create 2^16 networks (or 2^8 if ISP used /56)
2001:05a8:0001:0001::0 – 2001:05a8:0001:ffff::0/64
2001:05a8:94ad:0001::0 – 2001:05a8:94ad:ffff::0/64
2001:05a8:b002:0001::0 – 2001:05a8:b002:ffff::0/64
2001:05a8:ffff:0001::0 – 2001:05a8:ffff:ffff::0/64
Notes: SCRIPT:
The customer can subdivide the 16 bits as desired to number their internal /64 subnets. Several examples are shown here.
For a smaller organization, the ISP might assign a /56 prefix instead of a /64, which would still allow the customer to create 256 subnets (2^8 = 256).

## Slide 41: Subnetting Global Addresses
Apply 1 of these /64 prefixes to a router interface
  2001:05a8:0001:00a1::0 /64
Hosts per subnet (a /64 is a single host)
  2001:05a8:0001:00a1::1 – 2001:05a8:01a1:00a1:FFFF:FFFF:FFFF:FFFF/64
Notes: SCRIPT:
Applying one of these /64 subnet prefixes to a router interface allows the router to provide it to hosts on the subnet link so they can autoconfigure their IPv6 addresses.

## Slide 42: Addressing Tools
Examples of IP address tools (which support IPv6 too) for ISPs:
  IPAT http://nethead.de/index.php/ipat
  ipv6gen http://techie.devnull.cz/ipv6/ipv6gen/
  sipcalc http://www.routemeister.net/projects/sipcalc/
  freeipdb http://home.globalcrossing.net/~freeipdb/

## Slide 43
Implementing IPv6
Notes: SCRIPT:
This section provides an examples IPv6-related commands that can be used to configure and verify IPv6 implementations.

## Slide 44: Verifying IPv6
Command | Description
show ipv6 interface [brief] [type number] [prefix] | Displays the status of interfaces configured for IPv6. The brief keyword displays a brief summary. The prefix keyword displays the IPv6 neighbor discovery prefixes that are configured on a specified interface.
show ipv6 routers [interface-type interface-number] [conflicts] | Displays IPv6 router advertisement information received from on-link routers (those locally reachable on the link). The conflicts keyword displays information about routers advertising parameters that differ from the advertisement parameters configured for the specified interface on which the advertisements are received.
show ipv6 neighbors [interface-type interface-number ¦ ipv6-address ¦ ipv6-hostname ¦ statistics] | Displays IPv6 neighbor discovery cache information for the specified neighbors. The optional statistics parameter displays neighbor discovery cache statistics.
Notes: SCRIPT:
Many IPv6 show commands are available to verify IPv6 implementations. Most of them are similar to their IPv4 counterparts with the only difference being the replacement of the keyword “ip” with “ipv6” in the command. For example, the IPv6 version of the IPv4 show ip interface command is show ipv6 interface.
Some useful IPv6 show commands are listed here.
Note that the commands show ipv6 routers and show ipv6 neighbors are unique to IPv6.

## Slide 45: Troubleshooting IPv6
Command | Description
debug ipv6 nd | Displays messages associated with ICMPv6 neighbor discovery. ICMPv6 neighbor discovery is the IPv6 replacement for the IPv4 ARP.
debug ipv6 packet [access-list access-list-name] [detail] | Displays information associated with IPv6 packet processing. When an IPv6 access list is specified, only packets permitted by the ACL are displayed. The detail keyword displays more information.
Notes: SCRIPT:
Several useful IPv6 debug commands are also available to verify IPv6 implementations.

## Slide 46: Enable IPv6 Routing
Enable the forwarding of IPv6 unicast datagrams.
Router(config)#
ipv6 unicast-routing
This command is required before configuring any form of IPv6 routing (static or dynamic)
Also required to support autoconfiguration of end devices.
The no ipv6 unicast-routing disables IPv6 routing capabilities of the router.
Notes: SCRIPT:
The Cisco IOS ipv6 unicast routing command is required before implementing either static or dynamic routing with IPv6 global unicast addresses.
The command is not needed before configuring IPv6 interface addresses.
It is also required for the interface to provide stateless auto-configuration.
Configuring no ipv6 unicast-routing disables the IPv6 routing capabilities of the router and the router acts as an IPv6 end-station.

## Slide 47: Enable CEF for IPv6
Enable Cisco Express Forwarding (CEF) for IPv6 (CEFv6).
Router(config)#
ipv6 cef
An optional command, CEFv6 is an advanced Layer 3 IP switching technology for the forwarding of IPv6 packets.
  It is required for some other IPv6 features to operate.
  When enabled, network entries in the IPv6 routing table are reflected in the Forwarding Information Bases (FIBs).
  The IPv6 adjacency tables maintain Layer 2 next-hop addresses for all entries that are in each FIB.
Notes: SCRIPT:
The command ipv6 cef enables express forwarding and improves overall packet processing performance. It is disabled by default.

## Slide 48: Configuring IPv6 Unicast Addresses
Link-local (FE80::/10)
Address Assignment
Global Routable
Address Assignment
Static
IPv6 Address
IPv6 Unnumbered
Dynamic
Stateless Autoconfiguration
DHCPv6
Static
Dynamic
Automatically created (EUI-64 format) if a global unicast IPv6 address is configured
IPv6 Address
IPv6 Unicast
Address Assignment
Notes: SCRIPT:
Link-local and global unicast addresses can be assigned statically or dynamically. This section cover manual assignment of these addresses.

## Slide 49: Enable IPv6 on an Interface
Configure an IPv6 address and prefix.
Router(config-if)#
ipv6 address address/prefix-length [link-local | eui-64]
Command is used to statically configure an IPv6 address and prefix on an interface.
Notes: SCRIPT:
To configure a global or link-local address on a router interface use the ipv6 address command.
You may specify an actual global unicast or link-local address alllow the IOS to configure is using the EUI-64
The link-local parameter configures the address as the link-local address on the interface.
The eui-64 parameter completes a global IPv6 address using an EUI-64 format interface ID.

## Slide 50: Assigning a Link-Local Address
Link-local addresses are created:
  Automatically using the EUI-64 format if the interface has IPv6 enabled on it or a global IPv6 address configured.
  Manually configured interface ID.
    Manually configured interface IDs are easier to remember than EUI-64 generated IDs.
Notice that the prefix mask is not required on link-local addresses because they are not routed.
R2
R1
.2
R1(config)# interface fa0/0
R1(config-if)# ipv6 address FE80::1 ?
link-local use link-local address
R1(config-if)# ipv6 address FE80::1 link-local
R1(config-if)# end
R1#

## Slide 51: Assigning a Static Link-Local Address
  The output confirms the link-local address.
R2
FE80::1
R1
.2
R1# show ipv6 interface fa0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::1 [TEN]
No global unicast address is configured
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
MTU is 1500 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ND DAD is enabled, number of DAD attempts: 1
ND reachable time is 30000 milliseconds
ND advertised reachable time is 0 milliseconds
ND advertised retransmit interval is 0 milliseconds
ND router advertisements are sent every 200 seconds
ND router advertisements live for 1800 seconds
Hosts use stateless autoconfig for addresses.
R1(config-if)#

## Slide 52: Assigning a Static Global Unicast Address
Global Unicast IPv6 addresses are assigned by omitting the link-local parameter.
For example, IPv6 address 2001:1::1/64 is configured on R1’s Fast Ethernet 0/0.
  Notice that the entire address is manually configured and that the EUI-64 format was not used.
R2
R1
.2
R1(config)# ipv6 unicast-routing
R1(config)# interface fa0/0
R1(config-if)# ipv6 address 2001:1::1/64
R1(config-if)#
FE80::1

## Slide 53: Assigning a Static Global Unicast Address
R2
FE80::1
2001:1::1/64
R1
.2
R1# show ipv6 interface fa0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::1 [TEN]
Global unicast address(es):
2001:1::1, subnet is 2001:1::/64 [TEN]
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
MTU is 1500 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ND DAD is enabled, number of DAD attempts: 1
ND reachable time is 30000 milliseconds
ND advertised reachable time is 0 milliseconds
ND advertised retransmit interval is 0 milliseconds
ND router advertisements are sent every 200 seconds
ND router advertisements live for 1800 seconds
Hosts use stateless autoconfig for addresses.
R1#

## Slide 54: Configuring an EUI-64 IPv6 Global Address
Notice that by simply configuring a global unicast IPv6 address on an interface also automatically generates a link-local interface (EUI-64) interface.
R1# config t
R1(config)# int fa0/1
R1(config-if)# ipv6 add 2001::/64 eui-64
R1(config-if)# do show ipv6 interface fa0/1
FastEthernet0/1 is administratively down, line protocol is down
IPv6 is enabled, link-local address is FE80::211:92FF:FE54:E2A1 [TEN]
Global unicast address(es):
2001::211:92FF:FE54:E2A1, subnet is 2001::/64 [EUI/TEN]
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF54:E2A1
MTU is 1500 bytes
<output omitted>

## Slide 55: EUI-64 IPv6 Global Address – Example 2
R1(config)# interface loopback 100
R1(config-if)# ipv6 address 2001:8:85a3:4289::/64 eui-64
<output omitted>
R1# show ipv6 interface loopback 100
Loopback100 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::21B:D5FF:FE5B:A408
Global unicast address(es):
2001:8:85A3:4289:21B:D5FF:FE5B:A408, subnet is 2001:8:85A3:4289::/64 [EUI]
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF5B:A408
MTU is 1514 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ND DAD is not supported
ND reachable time is 30000 milliseconds
Hosts use stateless autoconfig for addresses.

## Slide 56: Assigning Multiple IPv6 Addresses
What would happen if we configured 2 different IPv4 addresses and 2 different IPv6 addresses on the same interface?
R2
R1
.2
R1(config)# interface fa0/0
R1(config-if)# ip address 10.20.20.1 255.255.255.0
R1(config-if)# ip address 10.10.10.1 255.255.255.0
R1(config-if)# ipv6 address 2001:1::1/64
R1(config-if)# ipv6 address 2002:1::1/64
R1(config-if)# end
R1#
FE80::1
2001:1::1/64

## Slide 57: Assigning Multiple IPv6 Addresses
The second IPv4 entry replaced the first entry.
  However, both IPv6 addresses have been assigned to the Fa0/0 interface.
Interfaces can have multiple IPv6 addresses assigned to them.
  These addresses can be used simultaneously.
R2
R1
.2
R1# show run interface fa0/0
Building configuration...
Current configuration : 162 bytes
!
interface FastEthernet0/0
ip address 10.10.10.1 255.255.255.0
duplex auto
speed auto
ipv6 address 2001:1::1/64
ipv6 address 2002:1::1/64
ipv6 address FE80::1 link-local
end
R1#
10.10.10.1/24
FE80::1
2001:1::1/64
2001:2::1/64

## Slide 58: Configuring IPv6 Unicast Addresses
Link-local (FE80::/10)
Address Assignment
Global Routable
Address Assignment
Static
IPv6 Address
IPv6 Unnumbered
Dynamic
Stateless Autoconfiguration
DHCPv6
Static
Dynamic
Automatically created (EUI-64 format) if a global unicast IPv6 address is configured
IPv6 Address
IPv6 Unicast
Address Assignment

## Slide 59: Enable IP Unnumbered
Enable IPv6 on an interface without an explicit IPv6 address.
Router(config-if)#
ipv6 unnumbered interface-type interface-number
Enables IPv6 processing on an interface without assigning an explicit IPv6 address to the interface.
The unnumbered interface will use the IPv6 address of the interface specified by the interface-type interface-number parameters as the source address of traffic from the configured interface.
  The interface specified in the command must be in the “up” state.

## Slide 60: Assigning IPv6 Unnumbered Interfaces
IPv6 supports unnumbered interfaces to enable IPv6 processing on an interface without assigning an explicit IPv6 address to the interface.
In this example, a loopback interface is created and configured with an IPv6 address.
  The Serial 0/0/0 interface is then configured to use the IPv6 address of the loopback interface.
S0/0/0
R1(config)# interface loopback 10
R1(config-if)# ipv6 address 2001:1::10/64
R1(config-if)# exit
R1(config)#
R1(config)# interface s0/0/0
R1(config-if)# ipv6 unnumbered loopback 10
R1(config-if)# no shut
R1(config-if)#
R1
Lo10: 2001:1::10/64
R2

## Slide 61: Assigning IPv6 Unnumbered Interfaces
  The output confirms that the Serial 0/0/0 interface uses the IPv6 address from interface loopback 10.
R1# show ipv6 interface s0/0/0
Serial0/0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::222:55FF:FE18:7DE8
No Virtual link-local address(es):
Interface is unnumbered. Using address of Loopback10
No global unicast address is configured
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF18:7DE8
MTU is 1500 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ICMP unreachables are sent
ND DAD is enabled, number of DAD attempts: 1
ND reachable time is 30000 milliseconds (using 16238)
Hosts use stateless autoconfig for addresses.
R1#
S0/0/0
R1
Lo10: 2001:1::10/64
R2

## Slide 62: Configuring IPv6 Unicast Addresses
Link-local (FE80::/10)
Address Assignment
Global Routable
Address Assignment
Static
IPv6 Address
IPv6 Unnumbered
Dynamic
Stateless Autoconfiguration
DHCPv6
Static
Dynamic
Automatically created (EUI-64 format) if a global unicast IPv6 address is configured
IPv6 Address
IPv6 Unicast
Address Assignment

## Slide 63: Enable Stateless Autoconfiguration
Enable the automatic configuration of IPv6 addresses.
Router(config-if)#
ipv6 address autoconfig [default]
Enables stateless autoconfiguration which:
  Automatically configures IPv6 addresses using the interface.
  Enables the IPv6 processing on the interface.
Addresses are configured depending on the prefixes received in RA messages.
(Optional) If the default keyword router is used it causes a default route to be installed using that default router.
  The keyword can be specified only on one interface.
Notes: An IPv6 router on a local link can send network information, such as the 64-bit prefix of the local link network and the default route, to all the nodes on the local link.
Hosts can autoconfigure themselves by appending their IPv6 interface identifier (in EUI-64 format) to the local link 64-bit prefix.

## Slide 64: Alter the Neighbor Detection Timeframe
Alter the neighbor detection parameter.
Router(config-if)#
ipv6 nd reachable-time milliseconds
Specifies the number of milliseconds that a remote IPv6 node is considered reachable.
Enables a router to detect unavailable neighbors more quickly.
  The milliseconds parameter (from 0 to 3,600,000) configures the amount of time that a neighbor sends an update to the router.
  Default is 0 milliseconds (unspecified time) in router advertisements and 30,000 (30 seconds) for the neighbor discovery activity.
  Caution: A very short time may consume more network bandwidth and processing resources.

## Slide 65: Statically Add a Neighbor
Add a neighbor router to the neighbor discovery cache.
Router(config)#
ipv6 neighbor ipv6-address interface-type interface-number hardware-address
Statically configures an entry in the IPv6 neighbor discovery cache, mapping the IPv6 address to the hardware address on an interface.

## Slide 66: Stateless Autoconfiguration
Router(config)#ipv6 unicast-routing
Router(config)#int fa0/1
Router(config-if)#ipv6 addr 2001:db8::/64 eui-64
Router(config-if)#ipv6 enable
Router(config-if)#no shut
Only the network part of the address is supplied
in the ipv6 address command
Notes: When configuring the interface, only the network portion is supplied in the command.
Stateless autoconfiguration is used on interfaces that have MAC addresses.
The ipv6 enable command automatically configures an IPv6 link-local unicast address on the interface while also enabling the interface for IPv6 processing.

## Slide 67: Stateless Autoconfiguration
Router’s fa0/1 interface generates its link-local address and global unicast address
Router#sho ipv6 int bri
FastEthernet0/0 [administratively down/down]
FastEthernet0/1 [up/up]
FE80::201:42FF:FE44:3C02
2001:DB8::201:42FF:FE44:3C02
Notes: The router automatically generates its link-local address (FE80).
The globally routable address is generated by stateless autoconfiguration (2001).
Notice that the show command includes “ipv6”

## Slide 68: Good Practice in IPv6 Addressing
Hosts should have globally routable addresses created with stateless autoconfiguration
  Use 2001 prefix
  Use /64 eui-64 to create them
Serial links between routers should not use globally routable addresses
  Use FC00 prefix and static addressing
  Use a prefix length /64
  However, the prefix length could also be, for example, /112

## Slide 69: IPv6 Connectivity on FR Multipoint Links
Just as for IPv4, IPv6 addresses must be mapped to DLCIs in Frame Relay.
This mapping can be:
  Dynamic using IPv6 inverse ARP
  Static using a frame-relay map interface configuration command.
Differences between IPv4 and IPv6:
  In IPv6, a map is usually needed for link-local addresses and global unicast addresses.
  In IPv6, the ipv6 unicast-routing command must be configured when a routing protocol is used across the Frame Relay network for the routers to exchange updates.

## Slide 70: IPv6 Multipoint FR Example
In this example topology, R1 connects to R2 and R3 over a multipoint Frame Relay connection.
Frame Relay
2001:12::1/64
.1
R2
R3
R1
2001:12::3/64
2001:12::2/64
DLCI: 103
DLCI: 301
DLCI: 201
DLCI: 102
S0/0/0
S0/0/0
S0/0/0

## Slide 71: IPv6 Multipoint FR Example
Configure the frame relay map on R1 to reach R2.
  R1 must use DLCI 102.
R1(config)# interface s0/0/0
R1(config-if)# frame-relay map ipv6 2001:12::2 102
R1(config-if)# do show frame-relay map
Serial0/0/0 (up): ipv6 2001:12::2 dlci 102(0x66,0x1860), static,
IETF, status defined, active
<output omitted>
R1#
Frame Relay
2001:12::1/64
.1
R2
R3
R1
2001:12::3/64
2001:12::2/64
DLCI: 103
DLCI: 301
DLCI: 201
DLCI: 102
S0/0/0
S0/0/0
S0/0/0

## Slide 72: IPv6 Multipoint FR Example
Configure the frame relay map on R2 to reach R1.
  R2 must use DLCI 201.
R2(config)# interface s0/0/0
R2(config-if)# frame-relay map ipv6 2001:12::1 201
R2(config-if)#
Frame Relay
2001:12::1/64
.1
R2
R3
R1
2001:12::3/64
2001:12::2/64
DLCI: 103
DLCI: 301
DLCI: 201
DLCI: 102
S0/0/0
S0/0/0
S0/0/0

## Slide 73: IPv6 Multipoint FR Example
Verify connectivity to R2 from R1.
R1# ping 2001:12::2
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 2001:12::2, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 56/57/60 ms
R1#
Frame Relay
2001:12::1/64
.1
R2
R3
R1
2001:12::3/64
2001:12::2/64
DLCI: 103
DLCI: 301
DLCI: 201
DLCI: 102
S0/0/0
S0/0/0
S0/0/0

## Slide 74: IPv6 Multipoint FR Example
Create a link-local address, an OSPF router ID, and then enable OSPFv3 on the S0/0/0 interface and identify R2 as an OSPF neighbor.
R1(config)# interface s0/0/0
R1(config-if)# ipv6 address FE80::1 link-local
R1(config-if)# exit
R1(config)# ipv6 unicast-routing
R1(config)# ipv6 router ospf 1
R1(config-rtr)# router-id 1.1.1.1
R1(config-rtr)# exit
R1(config)# interface s0/0/0
R1(config-if)# ipv6 ospf neighbor FE80::2
R1(config-if)# ipv6 ospf 1 area 0
R1(config-if)#
Frame Relay
2001:12::1/64
.1
R2
R3
R1
2001:12::3/64
2001:12::2/64
DLCI: 103
DLCI: 301
DLCI: 201
DLCI: 102
S0/0/0
S0/0/0
S0/0/0

## Slide 75: IPv6 Multipoint FR Example
On R2, configure similar commands and add a Frame Relay map statement pointing to R1 with the broadcast keyword.
R2(config)# interface s0/0/0
R2(config-if)# ipv6 address FE80::2 link-local
R2(config-if)# exit
R2(config)# ipv6 unicast-routing
R2(config)# ipv6 router ospf 1
R2(config-rtr)# router-id 2.2.2.2
R2(config-rtr)# exit
R2(config)# interface s0/0/0
R2(config-if)# ipv6 ospf neighbor FE80::1
R2(config-if)# ipv6 ospf 1 area 0
R2(config-if)# frame-relay map ipv6 FE80::1 201 broadcast
R2(config-if)#
Frame Relay
2001:12::1/64
.1
R2
R3
R1
2001:12::3/64
2001:12::2/64
DLCI: 103
DLCI: 301
DLCI: 201
DLCI: 102
S0/0/0
S0/0/0
S0/0/0

## Slide 76: IPv6 Multipoint FR Example
On R1, add a similar Frame Relay map pointing to R2.
  Notice that OSPF immediately forms the adjacency.
R1(config-if)# frame-relay map ipv6 FE80::2 102 broadcast
R1(config-if)#
*Aug 13 22:03:41.922: %OSPFv3-5-ADJCHG: Process 1, Nbr 2.2.2.2 on Serial0/0/0
from LOADING to FULL, Loading Done
R1(config-if)#
Frame Relay
2001:12::1/64
.1
R2
R3
R1
2001:12::3/64
2001:12::2/64
DLCI: 103
DLCI: 301
DLCI: 201
DLCI: 102
S0/0/0
S0/0/0
S0/0/0

## Slide 77: Reousrces: Who’s Got What % of the addresses
http://www.sixxs.net/tools/grh/dfp/
http://www.ipv6.org/

## Slide 78: Who’s Got What % of the addresses
http://www.sixxs.net/tools/grh/dfp/
http://www.ipv6.org
  http://www.arin.net/policy/nrpm.html#ipv6